## Slide 1: Maps and map interpretation An introduction for geoscientists
Produced by the University of Derby in conjunction with UKOGL

## Slide 2
This teaching package provides an introduction to maps and how to identify landforms using contours and cross-sections
It is designed primarily for A-Level and first year undergraduate geology and geography students who may have little experience of topographic maps, or for those who haven’t worked with them recently
Aims
Notes: If you are delivering this session to a class and want to incorporate the two practical sessions, print out multiple copies of Slides 50-52 beforehand and provide graph paper for drawing the cross-section

## Slide 3
Part 1 - Introduction to maps
  Title
  Key (sometimes called legend or explanation)
  Scales
  Contours
Part 2 – Map interpretation
  Contour patterns
  Cross-sections
Contents

## Slide 4: Part 1 - Introduction to maps
Maps are a 2-D representation of a 3-D world. They are a ‘bird’s eye’ view – as if the viewer is ‘flying’ above the land surface and looking down on it
They show how objects are distributed and their relative size
Maps are a very useful way of visualizing all sorts of data and they are a key tool for geoscientists

## Slide 5: The same map outline can be used to show different information, so it is important to identify the map title, key, scale and orientation
UK Bedrock Geology
UK Annual Mean Wind Speed
N
N
Title
Key
Scale
North Point
Notes: Questions for students:
Are the maps the same scale and orientation? Answer: Yes
What does the key for the Bedrock Geology Map tell you? Answer: There are three groups of rocks – sedimentary, metamorphic and igneous.

## Slide 6: Maps show how objects are distributed and their relative size
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
This is the area north of Derby that we will be focusing on later
Notes: Which is furthest west, Derby or Nottingham? Answer: Derby
Which occupies the greater area, Derby or Nottingham? Answer: Nottingham

## Slide 7: Scales
Show the distance on the map compared to the distance on the ground
It is important to choose an appropriate map scale for the task you are undertaking
Common scales include:
  1:30 000 000 (e.g. world map or atlas) 1:1 000 000 (e.g. country map) 1:50 000 (e.g. regional map) 1:10 000 (e.g. local map)
A map scale of 1:50 000 means:
  1mm on the map represents 50 000mm or 50m or 0.05km on the ground

## Slide 8
Scales with large numbers (e.g. 30 million) produce maps covering a large area in little detail
https://www.cia.gov/library/publications/the-world-factbook/docs/refmaps.html

## Slide 9: In contrast, on a 1:50 000 map, individual buildings, minor roads and contours are evident
N
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
1 km

## Slide 10
200 km
N
The scale bar shows a measurement on the map and the specific distance it represents on the ground
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
1 km
Galway to Dublin is about 200 km
Cowers Lane to Shottlegate is about 1 km
N
Notes: Stress that scale bars are useful when maps are being enlarged or reduced, because they maintain their proportion and can still be used (show reduced inset map as an example)

## Slide 11: Contours
Contours are lines joining points of equal value. This value on topographic maps is height (or elevation/altitude) above mean sea level (MSL)
Each successive contour represents an increase or decrease in constant value. Often every 5th contour will be in bold to help identification
Contours are normally associated with changes in height, but they can represent any parameter (e.g. thickness, pressure, rainfall). They can also be called iso-lines (e.g. isopachs, isobars, isohyets)
Notes: For Ordnance Survey maps the reference point for MSL is taken from Newlyn Harbour, Cornwall.

## Slide 12
Contours show the distribution and relative size of any measured value
Surface air pressure is measured in millibars and is shown here as isobars
Notes: What is the contour interval? Answer: 4 millibars
Where is the area of highest pressure? Answer: 1037 millibars over Austria
Where is the area of lowest pressure? Answer: 979 millibars over the Norwegian Sea

## Slide 13
Contours can show the distribution and relative size of any measured value
This map shows the thickness of the Earth’s crust (in kms)
This map shows rainfall data for Australia (in mm)

## Slide 14
N
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
1 km
Let’s return to topographic maps - on the map the land surface looks flat, but the contours indicate otherwise
View from Point X towards the SW, showing a valley and a hill in the distance
X
Notes: Learning to read contours takes practice. You have to visualize the 3-D shape described by the contour patterns.

## Slide 15
Contours never cross and will at some point close, although this may be off the map. Topographic contours that close in concentric patterns delineate hills or depressions
1 km
Notes: Does the diagram show a hill or a depression? Answer: A hill
Note that topographic contour values are written with the bottom of the number on the downhill side

## Slide 16
Contours are drawn perpendicular to the maximum slope, with the spacing between contours indicating the steepness of the slope
1 km
Notes: Which direction are the slopes facing? Answer: South
How steep is the steep slope? Answer: Not very – it only rises/falls 50m over a kilometre (about 3˚)

## Slide 17
Based on the shape of contours, landforms such as valleys and ridges can be recognised
Valley and stream
Ridge
1 km
Notes: Can you recognise a valley and a ridge?
Which direction is the stream flowing towards? Answer: South

## Slide 18
40m
30m
20m
10m
0 MSL
This image highlights the real shape of two hills and how they are shown on a contour map
Image from OS Map reading made easy. https://www.ordnancesurvey.co.uk/resources/map-reading/index.html

## Slide 19
You can watch a video explaining how to read contour lines on an Ordnance Survey map
Click here to play…
The Ordnance Survey website has further information on all aspects of maps and map reading, including how to work out grid references and take compass bearings https://www.ordnancesurvey.co.uk/resources/map-reading/index.html

## Slide 20
Practical exercise 1
Drawing contours

## Slide 21
1100m
970m
975m
900m
900m
900m
920m
800m
800m
1070m
880m
875m
950m
835m
835m
800m
700m
900m
Notes: Sometimes topographic maps are shown with height values at a given point, rather than contours. These are called ‘spot height’ maps and they are rather difficult to interpret. In order to get a better idea of the shape of the land surface the data can be contoured.

## Slide 22
800m
800m
700m
800m
700m
900m
750m
800m
850m
Then join up all the original and interpolated points of equal value to form contours.
Start by interpolating between individual points, labelling new values as you go.
750m
750m
750m
The easiest way to draw a contour map based on spot heights is to simply interpolate between the known values.
As you interpolate between points make sure you label the new values, as it quickly becomes very confusing if you don’t!
Then join identical values with smooth curves to create contours that simulate topography

## Slide 23
800
700
1100m
970m
975m
900m
900m
900m
920m
800m
800m
1070m
880m
875m
950m
835m
835m
800m
750
700m
900m

## Slide 24: Completing the contouring exercise
Based on the contour map you have created:
    Where is the highest ground?
    Where is the lowest area?
    Describe the major landforms
    Mark on the most likely course of a stream and determine in which direction it is flowing
Notes: The highest ground is in the north (>1100m).
The lowest area is in the SW, in the valley bottom (<700m).
The major landforms are a sinuous valley that trends SW-NE, then W-E, flanked by a broad ridge that trends NW-SE. The ground rises from the valley bottom to a high point in the north.
The stream is flowing from east to west.

## Slide 25
950
950
1000
1050
1100
1000
900
850
900
850
900
950
1000
1050
800
700
1100m
970m
975m
900m
900m
900m
920m
800m
800m
1070m
880m
875m
950m
835m
835m
800m
750
700m
900m
Notes: The highest ground is in the north (>1100m).
The lowest area is in the SW, in the valley bottom (<700m).
The major landforms are a sinuous valley that trends SW-NE, then W-E, flanked by a broad ridge that trends NW-SE. The ground rises from the valley bottom to a high point in the north.
The stream is flowing from east to west.

## Slide 26: Part 2 – Map interpretation
Contour patterns can be used to recognise distinctive landforms such as ridges, valleys and hills
Contours may appear as black or coloured lines on maps, and are often supported by colour shading to give an impression of relief
Cross-sections provide a useful way of visualizing the shape of the land surface, but care needs to be taken in their construction, particularly in terms of vertical exaggeration

## Slide 27
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
1 km
Previously we looked at the topography in this area – let’s take a closer look at the contours

## Slide 28
What is the contour interval? Locate the 150m contour between Shottle and Blackbrook
150m contour
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
1 km
The contour interval is 10m with bold lines every 50m

## Slide 29
If you walked along this contour, what would your route be like?
Flat, as long as you remain on the 150m contour
150m contour
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N

## Slide 30
Which direction is downhill from the 150m contour?
150m contour
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
200m contour
100m contour
Downhill

## Slide 31
What else about the contours help to determine the direction of slope?
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
The contour values are perpendicular to the slope, with the bottom of the number on the downhill side

## Slide 32
What does the hillside look like if you stand at Point A and look towards Point B?
B
A
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
1 km
It would go downhill to the stream and then uphill again to Point B

## Slide 33
100
200
300
400
500
600
700
800
900
100
200
A
B
Contour value (metres)
Distance (metres)
Valley with stream
0
No vertical exaggeration
This image shows a similar valley in the area, confirming the gentle slope angles
A useful technique to visualise landforms is to draw a cross-section. This one is between Points A and B on the previous map
The X axis represents distance and the Y axis height

## Slide 34
100
200
300
400
500
600
700
800
100
200
A
B
Contour value (metres)
Distance (metres)
Valley with stream
0
2x vertical exaggeration
When drawing cross-sections it is important to be aware how the scales affect your perception of slope angle
The purpose will dictate the scales you use. If the cross- section is to highlight relative changes in topography then a vertical exaggeration is fine, despite the fact that it increases the angles of all sloping lines
If there is a need to add sub-surface geology or calculate true slope angles, then there should be no vertical exaggeration

## Slide 35
Notice how the change in vertical exaggeration affects the angles of slope
Bear this in mind when drawing your own cross-sections and decide how much (if any) vertical exaggeration is required
Compare the effects of vertical exaggeration on the same cross-section

## Slide 36
You now know how to identify a sloping valley by the shape of the contours.
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
Uphill
They form a V-shape that points uphill

## Slide 37
There are lots of valleys on the map; mark them with an arrow pointing in the downhill direction
Arrows indicate downhill direction of valleys
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
Notes: This map shows some of the main valleys (not all have been marked)

## Slide 38
Notice that all the rivers are in valleys, but not all the valleys have a river. Why is this the case?
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
Arrows indicate downhill direction of valleys
Notes: There is no permanent water in these valleys, however in the past there was sufficient water that flowed along these routes to cause erosion and form the valley. Is there any time in the recent geological past when there was greater water flow in this area?

## Slide 39
What feature do the contours in the red area represent?
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
A broad, N-S trending ridge
Notes: Notice that the contours have a similar shape to a valley, but the V-shape points downhill

## Slide 40
It may help if you imagine you are standing at Point C on the 150m contour, looking towards Point D. Would you be able to see Point D?
We can draw a cross-section
to confirm our idea
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
C
D
Axis of ridge
Notes: Answer: No; Point D is at the same height (150m) as Point C, but the axis of the ridge is higher (at 175m).

## Slide 41
100
200
300
400
500
600
100
200
C
D
Contour value (metres)
Distance (metres)
Ridge
Cross-section showing the broad, gentle ridge between Points C and D
0
2x vertical exaggeration
Standing at Point C you would be unable to see Point D because the crest of the ridge is higher than Point D
Here some vertical exaggeration is appropriate because the relief is very subtle

## Slide 42
Practical exercise 2
Constructing cross-sections

## Slide 43
A
A’
Before constructing a cross-section, look at the contours and try to imagine what the surface topography looks like
Closely spaced contours showing a steep slope
Widely spaced contours showing less steep slopes compared to those in the east
Narrower range of contours between 140-160m indicate a relatively flat hill top
We will now draw our own cross-section between Cowers Lane (A) and Chevinside (A’)

## Slide 44
A
A’
Use graph paper to mark on every time a contour crosses the chosen line of section
85
90
95
100
105
110
150m
200m
100m
50m
Label each contour height and plot the value directly onto the Y-axis of the cross-section

## Slide 45
A
A’
Once all the contour heights along the section have been plotted the land surface can be added
50m
100m
150m
200m
This surface should be drawn free hand to give a natural shape that honours the contours
4x vertical exaggeration

## Slide 46
150m
100m
50m
0
200m
A
A’
1 km
2 km
3 km
A completed cross-section between A-A’
The vertical scale has been exaggerated in order to show the subtle relief. To calculate the vertical exaggeration, divide the horizontal scale (1cm to 200m) by the vertical scale (1cm to 50m)
So, 200/50 = 4x vertical exaggeration
West
East
Scale 1: 20 000
4x vertical exaggeration

## Slide 47
Comparison between a vertically exaggerated section and a true scale cross-section
200m
0
No vertical exaggeration
100m
150m
50m
200m
0
4x vertical exaggeration
The vertically exaggerated section provides a clearer representation of subtle landforms, the other a true representation of slope angles

## Slide 48
You have now been introduced to the basic elements of topographic maps
You have used contours to identify common landforms and begun to visualise them in 3-D
You can now construct cross-sections and understand the concept of vertical exaggeration
Learning outcomes

## Slide 49
Slide 50: print out at A4, in B/W, portrait format
Slide 51: print out at A4, in colour, portrait format
Slide 52: print out at A4, in colour, portrait format
Graph paper for constructing the cross-section
Handouts required for the practicals

## Slide 50
1100m
970m
975m
900m
900m
900m
920m
800m
800m
1070m
880m
875m
950m
835m
835m
800m
700m
900m

## Slide 51
© Crown Copyright/database right 2014. An Ordnance Survey/EDINA supplied service.
N
1 km

## Slide 52
A
A’